## Slide 1
Urban inference can
belong near demand
Cheap land pulls facilities outward. Interactive AI pulls compute toward users. Existing urban infrastructure may make that trade worthwhile.
01/07
Notes: The obvious answer for a data center is cheap land far from the city. Our project asks whether that changes for interactive AI inference. A request has to reach the model and return to the user, so the right location can depend on the network and the people it serves. We are testing an urban industrial site as a compact inference node, with slower work sent to a lower-cost regional facility. This is a siting hypothesis, not a measured latency result.
Source: `../docs/six_page_story.md`, Page 1.

## Slide 2
Density raises costs and creates synergies
02/07
COST
Land
Grid competition
Permits and community
SYNERGY
Users and networks
Workforce and heat customers
Reused industrial sites
Both sides need site-level proof.
Notes: Density cuts both ways. Urban land is contested, grid connections can be difficult, and permits and community impacts matter. The same area may also contain users, network facilities, skilled workers, industrial land and customers for waste heat. Our locator measures some physical proximity, especially grid, selected industry and treatment plants. It does not price land or prove a workforce, a heat contract or a fiber route. We therefore treat density as a reason to investigate specific sites, not as an automatic sustainability advantage.
Source: `../docs/six_page_story.md`, Page 2; `../README_DATA.md`.

## Slide 3
One site can connect six systems
03/07
GRID ASSETS
CARRIER ROUTES
INFERENCE USERS
HEAT CUSTOMERS
TREATMENT WATER
REUSED LAND
URBAN
INFERENCE
SITE
Proximity starts the case. Engineering and contracts complete it.
Notes: This diagram is the project thesis. A prospective inference site sits inside six surrounding systems. Grid assets may support an interconnection. Carrier routes and nearby users make a metro service plausible. Industrial neighbors might use low-grade heat. A treatment plant might support a reclaimed-water cooling design. Reusing an industrial footprint may reduce some new land or material needs. The current project maps candidate points and nearby source records. It does not prove any connection, available megawatts, usable water, heat demand or parcel rights. Each link is a due-diligence question.
Source: `../README_DATA.md`, Steps 1–12; `../outputs/validation/validation_report.md`.

## Slide 4
The locator turns national records into site evidence
04/07
190,976
EPA site records
8,479
screened candidates
INFRASTRUCTURE
INHERITANCE
INDUSTRIAL
SYMBIOSIS
Two independent axes
Local 5 km facility context
Notes: Here is what we have actually built. We start with 190,976 EPA RE-Powering records. Reported acreage and grid-distance thresholds yield 8,479 screened candidates. Each receives two separate opportunity scores. Infrastructure inheritance uses former power, transmission, substation, land and transport evidence. Industrial symbiosis uses selected manufacturing proximity and treatment-plant opportunity. The explorer exposes source values and a five-kilometer local ecosystem. Connectivity indicators sit in a separate preview, not in either score. The original 50-acre threshold also means compact urban parcels are missing from this candidate pool.
Source: `../outputs/validation/step1_summary.json`; `../outputs/validation/step7_summary.json`; `../README_DATA.md`.

## Slide 5
Two axes make urban tradeoffs visible
05/07
60
75
Inheritance
Symbiosis
Astoria
Salem
Indian Point
Davis Street
Astoria
78.46 / 93.21
Salem
61.19 / 79.99
Connectivity remains a separate exploratory view.
Notes: The separate axes make tradeoffs visible. Astoria and the Salem-area New England Power Company record both clear the current high-high thresholds. Indian Point has stronger inheritance but less surrounding symbiosis. Davis Street shows the opposite pattern and has an active facility-use question. Scores narrow the field. They do not settle parcel availability or data-center feasibility. The separate connectivity view tells us which facilities to investigate further, but its distance to a listed IXP-hosting building cannot establish user latency or a fiber contract.
Source: `../outputs/validation/step6_upper_right.csv`; `../outputs/validation/step11_selected_sites.csv`; `../outputs/validation/power_connectivity_review.md`.

## Slide 6
Astoria is the first due-diligence lead
06/07
ASTORIA
Queens, NY · EPA site 40157
78.46
inheritance
93.21
symbiosis
37
selected manufacturing
records within 5 km
Power capacity, fiber performance and parcel availability remain unverified.
Notes: Our first diligence lead is Astoria in Queens, EPA candidate 40157. It scores 78.46 for infrastructure inheritance and 93.21 for industrial symbiosis. The dataset counts 37 selected manufacturing facilities and three treatment-plant records within five kilometers. Its historical power match is name corroborated. These facts make Astoria worth a closer look. They do not mean that a parcel is free, that the utility can deliver the target load, or that the network route is fast. We recommend a region for verification, not a construction-ready site.
Source: `../outputs/validation/step6_upper_right.csv`; `../data/processed/site_features.parquet`; `../outputs/validation/validation_report.md`.

## Slide 7
The next decision requires measured feasibility
07/07
2030
VERIFY
Parcel, utility
and carrier checks
2040
PHASE
Inference nodes near demand
with contracted heat reuse
2050
REASSESS
Hardware, grid, water
and climate risk
Conditional implementation vision
Notes: The next step is a real feasibility test: identify a parcel, get utility capacity and timing, measure carrier paths to target users, and check heat demand and cooling design. If those gates clear, a metro inference node could be phased with demand and paired with regional offload. Over the longer term, hardware refresh, grid changes, water risk and climate resilience need repeated review. The current locator provides the shortlisting and evidence trail. The 2030 to 2050 path is an implementation vision, not a forecast of carbon or water savings.
Source: `../docs/six_page_story.md`, Pages 4–6.